## Slide 1: Wireless Networks
Lecture 9
Evolution of Wireless Networks (Part II)

## Slide 2: Key Specifications of 2G Technologies
 | IS-95/cdmaOne | GSM, DCS-1900 | IS-54, IS-136, PDC
Uplink frequencies | 824-849 MHz (US) 1850-1910 MHz (US pcs) | 890-915 MHz (EU) 1850-1910 MHz (US) | 800 MHz, 1500 MHz (Japan) 1850-1910 MHz (US pcs)
Downlink frequencies | 869-894 MHz US 1930-1990 MHz US pcs | 935-960 MHz EU 1930-1990 MHz US pcs | 869-894 MHz US 800, 1500 MHz Japan
Duplexing | FDD | FDD | FDD
Multiple access tech. | CDMA | TDMA | TDMA
Modulation | BPSK with Quad. | GMSK with BT.3 | DQPSK
Carrier bandwidth | 1.25 MHz | 200 KHz | 30 KHz
Data rate | 1.2288 MChips/s | 270.833 kbps | 48.6 kbps
Channels / carrier | 64 | 8 | 3
Speech Coding | CELP @ 13kbps EVRC @ 8 kbps | RPE-LTP @ 13 kbps | VSELP @ 7.95 kbps

## Slide 3: Evolution to 2.5G
2.5G upgrade must be compatible with 2G technology
Three different upgrade paths developed for GSM and two of these supports IS-136
  High speed circuit switched data (HSCSD)
  General packet radio service (GPRS)
  Enhanced Data rates for GSM Evolution (EDGE)
GPRS and EDGE supports IS-136
IS-95B upgrade for IS-95

## Slide 4: Wireless Networks Upgrade Paths
IS-95
GSM
IS-136 &
PDC
IS-95B
HSCSD
GPRS
EDGE
Cdma2000-1xRTT
Cdma2000-1xEV DVDO
Cdma2000-3xRTT
W-CDMA
TD-SCDMA
EDGE
All IP
NMT
AMPS
TACS
C450
1G
2G
2.5G
3G
4G

## Slide 5: HSCSD
Works in circuit switch mode.
Speed increased by allowing single user to use consecutive time slots in GSM standard
Relaxes error control coding algorithms specified in GSM increasing data rate from 9.600 to 14.400 Kbps
By using 4 slots, raw data rate of up to 57.6 kbps to individual user.
Ideal for dedicated streaming or real-time interactive web sessions

## Slide 6: GPRS
Packet-based data networks.
Well-suited for non real-time traffic like email, faxes, web browsing
Unlike HSCSD, GPRS allows multi-user channel sharing of individual radio channel and time slots and supports many more users.
GPRS units are automatically instructed to tune to dedicated GPRS channels and particular time slots for always-on access.
When all 8 slots are dedicated, data rate reaches to 171.2 kbps (8 x 21.4 kbps of raw un-coded data)

## Slide 7: EDGE (2.75G)
More advanced upgrade to 2G that requires addition of new hardware and software
Developed as a path to become eventual 3G high speed data access
New modulation 8-PSK in addition to GSM standard GMSK.
Allows nine different formats known as Multiple modulation and Coding Scheme (MCS)
Each MCS state may either use GMSK (low rate) or 8-PSK (high rate).
A family of MCS for each GSM slot and users can adaptively determine best MCS setting
User start first with max error protection and max data rate until the link has unacceptable outage or delay
By combining different channels (multi-carrier trans), EDGE provides upto several megabits per second data throughput.

## Slide 8: IS-95B or cdmaOne
IS-95/CDMA has a single upgrade path IS-95B for eventual 3G operation.
Dedicate multiple orthogonal user channels for specific users.
IS-95A support 64 users with data rate 14,400 Kbps
The raw data rate reaches to 8x14,400 = 115.2 kbps
Supports hard handoff procedure
  Allow units to search different radio channels without instruction from switch. User can rapidly tune to different BS.

## Slide 9: Evolution to 3G
Third generation of mobile phone standards based on the International Telecommunication Union (ITU) family of standards under the International Mobile Telecommunications programme, "IMT-2000"
3G technologies enable network operators to offer users a wider range of more advanced services while achieving greater network capacity through improved spectral efficiency. Services include
  broadband wireless data, all in a mobile environment.
  Typically, they provide service at 5-10 Mb per second.
The most significant feature of 3G is that it supports
  greater numbers of voice and data customers
  at higher data rates at lower incremental cost than 2G

## Slide 10: 3G Evolution
The community remain split into two camps
  GSM/IS-136/PDC
    The 3G evolution is wideband CDMA (W-CDMA)
    Also known as UMTS
  IS-95B or CDMA
    Evolution path is cdma2000
    Several variants exist but all based on IS-95B
ITU-2000 standards are separated into two major organizations reflecting two 3G camps
  3GPP: 3G partnership project for W-CDMA
  3GPP2: 3G partnership project 2 for cdma2000

## Slide 11: 3G W-CDMA (UMTS)
This standard has evolved under European Telecom. Standards Institute (ETSI).
Backward compatible with 2G standards GSM, IS-136 and PDC technologies as well as 2.5G
Bit level packaging of GSM data is retained, with additional capacity and bandwidth provided by new CDMA air interface
Always-on packet-based service for computers, entertainment devices and telephone.
Require expensive new BS equipments making installation slow and gradual

## Slide 12: 3G W-CDMA
Data rate supported up to 2.048 Mbps per user
  Allowing high quality data, multimedia, streaming audio (for stationary user).
Future version will support data rate in excess of 8 Mbps
Minimum spectral allocation of 5 MHz
Data rates from as low as 8 kbps to as high as 2 Mbps will be carried simultaneously on a single radio channel.
Each channel can support between 100 and 350 voice calls simultaneously depending on propagation conditions

## Slide 13: 3G cdma2000
Provides seamless and evolutionary upgrade path for 2G and 2.5G CDMA technology.
Centers on original 1.25 MHz radio channel
CDMA operators may seamlessly and selectively upgrade without changing entire BS equipment
The first 3G CDMA standard cdma2000 1xRTT using single channel (1x => multi-carrier)
Cdma2000 1x
  supports data rate up to 307 kbps in packet mode
  Can support up to twice as many users as 2G CDMA

## Slide 14: cdma2000
  No additional equipment needed, simply software and new channel cards at BS
Cdma2000 1xEV Evolution by Qualcomm
  Proprietary high data rate packet standard to be overlaid on existing
  CDMA 1xEC-DO dedicates the channel strictly to data user and support 2.4 Mbps per channel.

## Slide 15: cdma2000
Cdma2000 3xRTT
  The ultimate 3G solution relies upon multicarrier that gang adjacent channels together into 3.75 MHz.
  Three non-adjacent channels may be operated simultaneously and in parallel.
  Data rate in excess of 2 Mbps similar when compared to W-CDMA
Advocates of cdma2000 claim their standard much more seamless and less expensive upgrade path when compared to W-CDMA.

## Slide 16: 3G TD-SCDMA
In china, more than 8 millions GSM subscribers were added in just 1 month.
china’s desire to craft its own wireless vision.
Chinese CATT and Siemens jointly submitted IMT-2000 3G standard based on Time Division Synchronous Code Division Multiple Access
Relies on existing GSM infrastructure
1.6 MHz channel and smart antennas to yield more spectral efficiency.
5 ms frames divided into 7 slots allocated to single data only user or several slow users
TD-SCDMA allows easy upgrade to GSM.