## Slide 1: Wireless Networks

## Slide 2: Course Basics
Pre-requisite
Text books
  Data Communication and Networks
  Wireless Communication and Networks, 2nd Ed., W. Stalling.
  Wireless Communications: Principles and Practices, 2nd Ed., T. S. Rappaport.
  The Mobile Communications Handbook, J. D. Gibson

## Slide 3: Objectives of Course
Introduce
  Basics of wireless communication
  Evolution of modern wireless communication systems
  Wireless Networks
  Research issues in emerging wireless networks
Outcomes
  Adequate knowledge of wireless networks
  Able to carry research in different domains of wireless networks

## Slide 4: Course Syllabus
Introduction to wireless communication
Evolution of wireless communication systems
Medium access techniques
Propagation models
Cellular systems
  AMPS, IS-95, IS-136, GSM,
Wireless networks
  GPRS, EDGE, WCDMA, cdma2000, Mobile IP, WLAN and Bluetooth
Emerging networks
  WiMAX, MANET, WSN

## Slide 5: Introduction to Wireless Communication
The Wireless vision
Radio Waves
Channel Capacity
Signal-to-Noise Ratio
EM Spectrum

## Slide 6: The Wireless vision
What is wireless communication?
What are the driving factors?
  An explosive increase in demand of tetherless connectivity.
  Dramatic progress in VLSI technology
    Implementation of efficient signal processing algorithms.
    New Coding techniques
  Success of 2G wireless standards (GSM)
Notes: What is wireless communication?
WC is one of the most vibrant areas of communication field today. While it has been a topic of study since 1960s but the last decade has seen a surge of research activities in this area. This is due to influence of several factors
First there has been an explosive increase in demand of tetherless connectivity, mainly by cellular telephony.
Second the dramatic progress in VLSI technology has enabled implementation of efficient signal processing algorithms and coding techniques
When two parties communicate without having any physical contact or medium of communication
There are several driving factors of its popularity.
People want connectivity anywhere anytime for example, at airports, hotels, customers place, or group of people wants to share data at any location. Such requirements have made the wireless connectivity indispensable.
Keep in mind that the course mainly focuses on wireless networks rather than communication techniques.

## Slide 7: Wired Vs. Wireless Communication
Wired | Wireless
Each cable is a different channel
One media (cable) shared by all
Signal attenuation is low
High signal attenuation
No interference
High interference
noise; co-channel interference; adjacent channel interference

## Slide 8: Why go wireless ?
Advantages
  Sometimes it is impractical to lay cables
  User mobility
  Cost
Limitations
  Bandwidth
  Fidelity
  Power
  (In) security

## Slide 9: Electromagnetic Signal
Function of time
Can also be expressed as a function of frequency
  Signal consists of components of different frequencies
Notes: EM signal is used as a means to transmit information. EM is a function of time but it can also be expressed as a function of frequency
That is the signal consists of components of frequencies. However, the frequency domain view of a signal is more important.

## Slide 10: Time-Domain Concepts
Analog signal - signal intensity varies in a smooth fashion over time
  No breaks or discontinuities in the signal
Digital signal - signal intensity maintains a constant level for some period of time and then changes to another constant level
Periodic signal - analog or digital signal pattern that repeats over time
  s(t +T ) = s(t ) - ∞< t < + ∞
    where T is the period of the signal
Aperiodic signal - analog or digital signal pattern that doesn't repeat over time
Notes: In time domain, the signal can be either analog or digital.
In analog siganl, the signal intensity varies in a smooth fashion over time. For example in speech, voice changes its amplitude/intensity over time with continuous change.
Digital signals are binary 0s, 1s or text
Periodic signal: analog periodic signal like sine wave and digital periodic signal like square wave

## Slide 11: Time-Domain Concepts
Peak amplitude (A) - maximum value or strength of the signal over time; typically measured in volts
Frequency (f )
  Rate, in cycles per second, or Hertz (Hz) at which the signal repeats
Period (T ) - amount of time it takes for one repetition of the signal
  T = 1/f
Phase () - measure of the relative position in time within a single period of a signal
Notes: General sine wave can be represented by three parameters

## Slide 12: Time-Domain Concepts
Wavelength () - distance occupied by a single cycle of the signal
  Or, the distance between two points of corresponding phase of two consecutive cycles
   = vT
Sine wave
Square wave

## Slide 13: Time-Domain Concepts
General sine wave
  s(t ) = A sin(2ft + )
Figure shows the effect of varying each of the three parameters
  (a) A = 1, f = 1 Hz,  = 0; thus T = 1s
  (b) Reduced peak amplitude; A=0.5
  (c) Increased frequency; f = 2, thus T = ½
  (d) Phase shift;  = /4 radians (45 degrees)
note: 2 radians = 360° = 1 period

## Slide 14: Sine Wave Parameters

## Slide 15: Frequency-Domain Concepts
Fundamental frequency - when all frequency components of a signal are integer multiples of one frequency, it’s referred to as the fundamental frequency
Spectrum - range of frequencies that a signal contains
Absolute bandwidth - width of the spectrum of a signal
Effective bandwidth (or just bandwidth) - narrow band of frequencies that most of the signal’s energy is contained in

## Slide 16: Frequency-Domain Concepts
Any electromagnetic signal can be shown to consist of a collection of periodic analog signals (sine waves) at different amplitudes, frequencies, and phases
The period of the total signal is equal to the period of the fundamental frequency

## Slide 17: Relationship between Data Rate and Bandwidth
The greater the bandwidth, the higher the information-carrying capacity
Conclusions
  Any digital waveform will have infinite bandwidth
  BUT the transmission system will limit the bandwidth that can be transmitted
  AND, for any given medium, the greater the bandwidth transmitted, the greater the cost
  HOWEVER, limiting the bandwidth creates distortions

## Slide 18: About Channel Capacity
Impairments, such as noise, limit data rate that can be achieved
For digital data, to what extent do impairments limit data rate?
Channel Capacity – the maximum rate at which data can be transmitted over a given communication path, or channel, under given conditions

## Slide 19: Concepts Related to Channel Capacity
Data rate - rate at which data can be communicated (bps)
Noise - average level of noise over the communications path
Error rate - rate at which errors occur
  Error = transmit 1 and receive 0; transmit 0 and receive 1

## Slide 20: Nyquist Bandwidth
For binary signals (two voltage levels)
  C = 2B
With multilevel signaling
  C = 2B log2 M
    M = number of discrete signal or voltage levels
Notes: Give an example for M = 8 and B 3100 C = 18600
So the data rate can be increased by increasing the number of different signal elements. This places an extra burden on receiver

## Slide 21: Signal-to-Noise Ratio
Ratio of the power in a signal to the power contained in the noise that’s present at a particular point in the transmission
Typically measured at a receiver
Signal-to-noise ratio (SNR, or S/N)
A high SNR means a high-quality signal, lower number of required intermediate repeaters
SNR sets upper bound on achievable data rate
Notes: SNR expresses the amount in decibels that the intended signal exceeds the noise level.

## Slide 22: Shannon Capacity Formula
Equation:
Represents theoretical maximum that can be achieved
In practice, only much lower rates achieved
  Formula assumes white noise (thermal noise)
  Impulse noise is not accounted for
  Attenuation distortion or delay distortion not accounted for
Notes: Nyquist formula indicates that all other things being equal, doubling the bandwidth doubles the data rate
Shannon investigate relationship of data rate with bandwidth and noise.
From the Eq., data rate can be increased either by increasing bandwidth or signal strength.
LowerF = 3Mhz, UpperF = 4 MHz SNR = 24 then
B = 4 – 3 = 1 MHz
SNRdb = 10log10 (24) = 251
C = 10^6 x log2(1 + 251)
Approx. 10^6 x 8 bps = 8 Mbps
For this data rate, the number of signal levels by Nyquist formula are
M = 16

## Slide 23: EM Spectrum

Propagation characteristics are different in each frequency band
UV
1 MHz
1 kHz
1 GHz
1 THz
1 PHz
1 EHz
infrared
visible
X rays
Gamma rays
AM radio
S/W radio
FM radio
TV
TV
cellular
LF
HF
VHF
UHF
SHF
EHF
MF


30kHz
300kHz
3MHz
30MHz
300MHz
30GHz
300GHz
10km
1km
100m
10m
1m
10cm
1cm
100mm
3GHz
902 – 928 Mhz
2.4 – 2.4835 Ghz
5.725 – 5.785 Ghz
ISM band
Notes: 20 Hz to ~14 kHz, acoustic — normal range of adult human hearing (most children and some animals perceive sounds outside this range, most teens and children can hear frequencies from 14 kHz up to ~16 kHz where most adults can't)
530 kHz to 1.710 MHz, electromagnetic — AM radio broadcasts
42 MHz to 260 MHz, electromagnetic — VHF terrestrial TV broadcast channels
88 MHz to 108 MHz, electromagnetic — FM radio broadcasts
902 MHz to 928 MHz, common cordless telephone frequency in the US
0.8 to 2.3 GHz, (electromagnetic) - mobile phone conversation channels.
2.4 GHz, (electromagnetic) - microwave ovens, Wireless LANs and cordless phones (starting in 1998).
5.8 GHz, cordless phone frequency introduced in 2003
428 THz to 750 THz, electromagnetic — visible light, from red to violet
30 Petahertz (PHz), electromagnetic — x-rays
300 Exahertz (EHz) and above - gamma rays

## Slide 24: Design Challenges
Two fundamental aspects of wireless communication
  Channel fading
    Multipath fading
    Path loss via distance attenuation
    Shadowing by obstacles
  Interference
    Multiple transmitters to a common receiver
    Multiple transmitters to multiple receivers
Notes: In wireless telecommunications, multipath is the propagation phenomenon that results in radio signals' reaching the receiving antenna by two or more paths. Causes of multipath include atmospheric ducting, ionospheric reflection and refraction, and reflection from terrestrial objects, such as mountains and buildings.

## Slide 25
The primary concern in wireless systems is to increase the reliability of air interface.
This is achieved by controlling the channel fading and interference.
Recently the focus has shifted to spectral efficiency.

## Slide 26: Summary
EM seen in domain of time and frequency
Analog and digital signal
Periodic and aperiodic signal
Frequency, amplitude and wavelength of signal
Fundamental frequency
Channel capacity
  Nyquist formula
  Shannon formula
EM Spectrum
Design challenges in wireless communication